## Slide 1
Myth busting renewable energy. ​
Professor Kylie Catchpole and Professor Ken Baldwin,
ANU Grand Challenge: Zero-Carbon Energy for the Asia-Pacific

## Slide 2: International Energy Agency report, May 2021
“The world has a viable pathway to building a global energy sector with net-zero emissions in 2050, but it is narrow and requires an unprecedented transformation of how energy is produced, transported and used globally”
From today, no investment in new fossil fuel supply projects
By 2035, no sales of new internal combustion engine passenger cars
By 2040, the global electricity sector has already reached net-zero emissions.

## Slide 3
Global annual net new capacity per annum
There is a revolution happening in the type of energy that is being installed

## Slide 4
Solar and wind are the largest contributors across all sectors, not only energy

## Slide 5
IEA, World Energy Outlook 2019
Solar projected to reduce emissions by 3Gt CO2 by 2030, approximately equal to emissions from all the cars on the road today
Wind will reduce emissions by 2Gt, EVs by around 1Gt.
IEA Net-zero roadmap 2023

## Slide 6: Myth 1: Renewables can’t meet demand and keep the grid stable 24/7 Myth 2: Renewables take up too much land Myth 3: Renewables are too expensive Myth 4: Renewables can’t replace our energy exports

## Slide 7: Myth 1: Renewables can’t meet demand and keep the grid stable 24/7

## Slide 8: Continually growing solar deployment
1 GW
760 GW
1 terawatt
>900 GWp by 2021
Compared to 40 GWp in 2010
Factor of 17 increase in 10 years (average yearly growth rate of 33%)

## Slide 9
50-70% of global electricity demand by 2050 requires 25% growth rate to continue, and then decrease to replacement rate.
Requires annual installations globally to increase from 0.3TW to 3TW.
Haegel et al., Science 2023
DOI: 10.1126/science.adf6957
Global required new capacity

## Slide 10: Reliability
Sector coupling: power, transportation, heating
Geographical dispersion
Technical diversity
  Wind, photovoltaics
Mass storage
  Pumped hydro
  Electric car batteries
  Hydrogen
  Batteries

## Slide 11
How much will we need?
AEMO draft 2024 integrated system plan

## Slide 12: What about storage? Power vs energy
energy
POWER

## Slide 13
How much storage will we need?
AEMO draft 2024 integrated system plan

## Slide 14
Long duration energy storage (LDES) > 8 hrs
Snowy hydro 5.5 GW
Snowy 2.0 increase to 7.5 GW
Snowy 2.0 = 350GWh or
175 hrs of operation
power (GW) x time (h) = energy (GWh)
Energy balancing – over days

## Slide 15: Global pumped hydro atlas
https://re100.eng.anu.edu.au/

## Slide 16: Battery storage
Batteries can respond very fast to disturbances.
Good for
short-term storage (hours)
helping with transmission constraints
Maintaining grid stability

## Slide 17
Batteries can respond very fast – so now largest frequency control and ancillary services (FCAS) provider in the NEM.

## Slide 18
Modelled generation of 100% renewable electricity in Australia
Seasonal variability can be managed with pumped hydro, more renewables and transmission – but we need to get moving
Modelling from Bin Lu, ANU

## Slide 19: Myth 2: Renewables take up too much land

## Slide 20
100% renewable energy (zero fossil fuels) means 60 m2 of solar panel per person
Fraction of the world’s land: 0.1%
(at developed country energy consumption rates)

## Slide 21
Macarthur wind farm, Victoria, 420 MW
112m rotor diameter, 3MW

## Slide 23
¾ of people live in the sunshine belt (+/- 35°)
High & consistent solar, no cold winters
Most of the growth in population, energy consumption and emissions
Solar availability – redder is better
Australia’s opportunity for leadership

## Slide 24: Myth 3: Renewables are too expensive

## Slide 25: Learning rates
Source: CSIRO
Number of units produced
Competing Technology

## Slide 26: Technology learning rates: solar PV
Time
Source: 13th International Technology Roadmap for PV (2022)
1/500th
price per
module!
Doubling the units of production decreases the price by 24.1%
This represents a compound annual growth rate (CAGR) of 33% for the last 40+ years!

## Slide 27: Learning rates for various technologies

## Slide 28: Levelised cost of electricity (LCOE)
It = Investment in year t Et = Electricity generation
Mt = Operations and maintenance r = Discount rate
Ft = Fuel expenditure n = Life of system (amortisation)
Caution: assumes
plug-and-play !
LCOE
Learning rate

## Slide 29: Australia: solar and wind now cheaper than coal
Wind
& PV
Wind & PV
+ storage
+ transmit
Fossil fuels
Fossil
fuels
+ CCS
ACT 2020
wind auction
$45/MWh
fixed price
($35-37 in constant $)
Present
LCOE
GenCost 2023/4
CSIRO & AEMO

## Slide 30: How high can renewables go?
LCOE is only plug and play.
The higher the penetration of variable renewables (>50 %), the higher the cost to cover intermittency:
  Overbuild supply
  Build additional storage capability
  Build additional network infrastructure
At 100% RE, adds 50%
to LCOE -
but still cheaper than coal or gas
}

## Slide 31
Australian Renewable Energy Pipeline
Source:
Clean Energy Regulator
Low large-scale investment <2017 because of govt. policy uncertainty
99% of new generation in Australia is renewable. Australia has installed ~6GW p.a. solar and wind for last 5 years, >3GW p.a. at utility scale - despite past government policy uncertainty

## Slide 32: Myth 4: Renewables can’t replace our energy exports

## Slide 33
Australia’s current energy trade
Most of Australia’s energy trade is with the Asia-Pacific
33
+ 4,933 tonnes Uranium = ~ 2,000 PJ
Source: DCCEEW Australian Energy statistics, Table J, 2023.

## Slide 34
Australia’s top commodity exports 2021
34
Chart: A$ billions
| iron ore | coal | LNG | alumina
 | 103 | 55 | 48 | 9
Higher education
Source:
DFAT trade and investment at a glance, 2021

## Slide 35
$10m ANU-funded + industry + govt.
5-year program 2019 - 2023
Research projects:
  Hydrogen fuels
  Renewable electricity systems
  Green metals
  Policy & governance in the Asia-Pacific
  Indigenous engagement
ANU Grand Challenge:
Zero-Carbon Energy
for the Asia-Pacific

## Slide 36
Australia’s current export emissions profile
Chart: Mt CO2-e
| Thermal coal | LNG | Iron ore | Bauxite and alumina | Australia's domestic emissions (all sectors)
 | 511.0348 | 209.6835 | 1032.8245 | 214.9014 | 529
Consequential emissions
from benchmark exports
Total emissions = 1,969 MtCO2e/y
~ 3.7 x Australia’s domestic emissions
Notes: MtCO2e/y = megatonnes of carbon dioxide equivalent per year

## Slide 37: Australia’s solar resource
World Bank Group global solar atlas 2020 https://globalsolaratlas.info
Double that of northern latitudes

## Slide 38
A future Australian export scenario
Export the same amount of energy (PJ) as now:
80% as hydrogen (65 Mt/year)
20% renewable electricity (540 TWH/y)
Mine the same amount of ore and export:
510 Mt/y as green steel (6 Mt/y steel now)
18 Mt/y as green aluminium (2 Mt/y Al now)
Total renewable electricity required
7,040 TWh/y
27 x Australia’s present electricity generation!
Add 100% domestic RE + 200% in electrification
= 2,700 + 100 + 200 = 3,000% renewables!
Even if only 10% of exports are realized, this still doubles Australia’s zero-emissions electricity future i.e. 600%.
Same ores
Same energy
20% 80%
Key message: on and off-grid renewables for export may dominate – and influence price and supply in – the domestic electricity sector
Notes: PJ = petajoules
Mt/y = megatonnes per year
TWh/y = terawatt hours per year

## Slide 39
Future NEM
Green energy exports double NEM capacity
(ignoring off-grid hydrogen)
AEMO draft 2024 ISP key capacity scenarios:
Progressive (slow)
Step change (favoured by most stakeholders)
Green energy exports

## Slide 40: Proposed H2 + e- export projects >120GW new RE
H2,NH3
e-
Australian Renewable Energy Hub – 26GW
Yara Pilbara – 5GW
Province HyEnergy – 8 GW
Murchison Renewable H2 – 5GW
Infinite Green Energy – 1GW
Western Green Energy Hub – 50GW
SA hydrogen export terminal – 0.25GW
Forrest Future Industries – 2GW
Stanwell – 3GW
Hydrogen Utility – 3GW
Sun Cable – 20GW (electricity)
NH3
H2
H2
NH3
H2
e-
H2
H2
H2
H2

## Slide 41: Green Steel
Hydrogen
Australian exports
Renewables